THE ROLE OF THE THERMAL INDUCED RESIDUAL

STRESSES IN A SINGLE FIBRE THERMOPLASTIC

MODEL COMPOSITE

C.C.Wang1, J.L.Thomason2 and F.R.Jones1

1 Department of Engineering Materials, University of Sheffield, S1 3JD, UK:

2 Department of Mechanical Engineering, University of Strathclyde, 75 Montrose

Street, Glasgow, G1 1XJ,U.K

f.r.jones@sheffield.ac.uk

SUMMARY

In this paper, the introduction of the thermal induced residual stresses into a single fibre composite was investigated by phase-stepping photoelasticity. It has been demonstrated that stress transfer occurs through a thermally induced interfacial shear stress. On the axial loading of the composite, the stress at which the birefringence is extinguished can be used to estimate the magnitude of the interfacial shear stress.

Keywords: Residual stress, glass fibre, polyamide, stress transfer mechanism