Partnership for Research In Marine Renewable Energy
7th PRIMaRE Conference
7-8 July 2020
An Experimental and CFD Study of the Extreme Waves Impact on OC3-Hywind Spar Floating Offshore Wind Turbine
Yang Zhou, Saishuai Dai, Sandy Day, Qing Xiao, Michael Coppini
Department of Naval Architecture, Ocean and Marine Engineering
University of Strathclyde

---
Introduction
Extreme Wave modelling:
Focused Wave & Irregular Wave
Why focused wave?
Studies on:
Hywind Spar floater
Wave tank test & CFD modelling
A photo of FOWT survives in huge waves
A photo of Statoil’s
Hywind Spar FOWT

---
Experimental Setup (Structural Properties)
	NREL OC3 Hywind[1]	Present model at KHL
Scaled Model	Prototype	Yes
Scaled Factor	N/A	1:74
Platform Mass, including ballast	7,466,330 kg	19.916 kg / (Tower included)
CM location below SWL	-89.9155 m	-1.0924 m
Platform Roll inertia	4,229,230,000 kg*m2	11.284 kg*m2
Platform Pitch inertia	4,229,230,000 kg*m2	11.284 kg*m2
Platform Yaw inertia	164,230,000 kg*m2	N/A
Natural Frequency	Heave: 27.5s / Pitch: 23.9s	Heave: 3.83(33.0)s / Pitch: 3.60(31.0)s
Mooring Lines settings	3 catenary lines	4 soft mooring lines
A photo of the scaled (1:74)
spar model in KHL (Present)
1. Jonkman, J., 2010, "Definition of the Floating System for Phase IV of OC3," National Renewable Energy Lab.(NREL), Golden, CO (United States).
32 Duan, F., Hu, Z., and Niedzwecki, J. M., 2016, "Model test investigation of a spar floating wind turbine," Marine Structures, 49, pp. 76-96.

---
Experimental Setup (Loading Cases)
Test Metrix:
  - Free Decay Tests
  - Wave Excitation: Regular, Focused, Irregular (Interests)
    - JONSWAP spectrum with identical wave peak period

---
WaveTank Data analysis (Pitch Motions)
FW001
Low Pass Filtering Cuttoff Freq. : 4Hz
Focused Wave:
Free Decay motions after Tf
Irregular Wave:
Stochastic phenomenon
IW001

---
WaveTank Data analysis (FW001)
Frequency Domain (PSDs)
Time Domain
Wavelet analysis[2]
[2] Lin, E.-B., and Liu, P. C., 2004, "A discrete wavelet analysis of freak waves in the ocean," Journal of Applied Mathematics, 2004(5), pp. 379-394.
Wave peak period
Pitch natural frequency
 Very Low frequency range

---
WaveTank Data analysis (Pitch PSDs)
Focused/Irregular waves
Same elapsed time selection: 200s
Nonlinear effect observed near second-order difference frequency

---
WaveTank Data analysis (RAOs)
Obtained from FW001/IW001
Agreed well near North sea wave periods(scaled) :0.4Hz < Freq. < 0.8Hz
Discrepancy of RAOs near platform natural frequency (viscous damping; wave-wave interaction)

---
CFD modelling (Methodology)
CFD solver “waveDyMFoam” in OpenFOAM[3][4]
Wave generation: Toolbox “waves2Foam”
  - Wave theory: First-order irregular waves
  - Identical target wave spectrum to wave tank
Simulation cases:
  - Focused waves (Code validation)
  - Irregular waves not modelled
[3]Jacobsen, N.G., Fuhrman, D.R., Fredsøe; A wave generation toolbox for the open-source CFD library: OpenFoam® (2012) International Journal for Numerical Methods in Fluids, 70 (9), pp. 1073-1088.
[4] Zhou, Y., Xiao, Q., Liu, Y., Incecik, A., Peyrard, C., Li, S., and Pan, G., 2019, "Numerical modelling of dynamic responses of a floating offshore wind turbine subject to focused waves," Energies, 12(18), p. 3482.

---
CFD settings (Boundary Conditions)
X (Surge)
Y (Sway)
4.0m
6.0 m
Wave Direction
Inlet Relaxation
Outlet Relaxation
6.0m
9.0m
Inlet
 = 0
Outlet
 = 0
= (0, 0, 0)
 = 0, = 0
 = 0, = 0

---
CFD settings (Computational Meshes)
Entire computational mesh
Mesh motion handling
Built-in sliding mesh technique in OpenFOAM
Mesh size: 2.12 Million
Not allowed to translate on Surge
To model 4 modified soft mooring lines
Mesh refinement near the free surface and the spar platform

---
Results (FW001, Motions)
Captured commendably between CFD and experimental
Discrepancy due to
mooring lines modelling
Wave-wave interaction

---
Results (FW001, PSDs)
Agreed well near incident wave energy range
Difference under floater natural frequency

---
Conclusions
Experimental: Compared between focused waves and Irregular waves RAOs
  - Capture similar peak value in both wave types in time domain
  - RAOs variance under floater natural frequency
CFD: Difference between CFD and wave tank data
  - Mooring Line modelling: CFD (allow surge) Tank (soft mooring)
  - Nonlinear loads calculation

---
Thank you for your attention!

---
Wavelet analysis (additional)
The traditional Fourier technique may not be suitable for non-stationary sequences[2], i.e., focused wave
Continuous wavelet transformation is applied to detect the time-frequency characteristics of the data under focused wave
Window function selection: Morlet wavelet
Time domain results selection: 80s-140s
[4] Lin, E.-B., and Liu, P. C., 2004, "A discrete wavelet analysis of freak waves in the ocean," Journal of Applied Mathematics, 2004(5), pp. 379-394.